## Slide 1: NVIDIA-Certified Hypervisor Program
June 11, 2026

## Slide 2: Context/Opportunity
Enterprises are virtualizing GPU workloads at scale and demanding performance parity with bare metal*
Customers want assurance that their hypervisor stack is validated and optimized for NVIDIA GPUs.
Red Hat has already done the work required - this program gives you hardware access and a validation framework to demonstrate and stay competitive.
*Whitepaper: Optimizing VM Configuration for Performant AI Inference

## Slide 3: Pgm Goals & Overview
Mission
Enable Hypervisor ISVs to validate that their GPU-optimized virtualization platforms & infra SW stacks can deliver near bare metal performance for Compute/AI workloads using NVIDIA-provided HW, curated validation suites, and control stack baselines that evolves with NVIDIA’s HW roadmap.
Goals/Objectives
Establish a standardized performance baseline that enables consistent validation across Hypervisor ISVs & partners
Access to latest NVIDIA platforms with a turnkey validation suite- deploy, run and validate.
Provide NVIDIA-backed validation that hypervisor partners can use to demonstrate AI readiness for virtualized Compute/AI workloads
Ongoing partnership tied to NVIDIA's roadmap so partners can revalidate with latest GPU architectures

## Slide 4: Program Tracks

## Slide 5: Track I- x86 Servers
Phase I: Single Node
Phase II: Multi Node
NVIDIA-Certified Hypervisor
8-GPU VM on a Hopper HGX node with all PCIe devices passed through
Partner is recognized as “NVIDIA-Certified Hypervisor” by NVIDIA upon successful completion of multi-node x86 validation
Two 8-GPU VMs, one each on two identical Hopper HGX nodes configured in full passthrough

## Slide 6: Track II - ARM Servers
GB200 NVL Compute Tray
NVIDIA-Certified Hypervisor
4-GPU VM on an GB200 NVL4 Tray with all PCIe devices passed through
Partner is recognized as “NVIDIA-Certified Hypervisor” by NVIDIA upon successful completion of single-node ARM validation

## Slide 7: Validation Suite & Key Metrics

## Slide 8: X86 Validation Test Suite & Key Metrics
Tests | What it measures | Metric | Phase I- Single Node x86 | Phase II- Multi Node x86
NCCL | GPU-to-GPU collective communication | Avg Bus BW or Throughput (GB/s) |  | 
NV Bandwidth | GPU/CPU/memory bandwidth | Bandwidth (GB/s) |  | 
GPU Stream | GPU memory bandwidth for streaming operations | Throughput (MB/sec) |  | 
HPL | Floating-point compute performance (FLOPS) | GFLOPS |  | 
cublas Matrix Multiplication | GPU compute performance for linear algebra operations | GFLOPS |  | 
LLM Perf | LLM inference throughput/latency | Throughput (tokens/sec)) | llama-3-70B | DeepSeek R1
GPU Direct RDMA | Cross-node GPU-to-GPU via RDMA | Throughput BW (GB/s) |  | 

## Slide 9: ARM Validation Test Suite & Key Metrics
Tests | What it measures | Metric | Single GB200 NVL Compute Tray
NCCL | GPU-to-GPU collective communication | Avg Bus BW or Throughput (GB/s) | 
NV Bandwidth | GPU/CPU/memory bandwidth | Bandwidth (GB/s) | 
GPU Stream | GPU memory bandwidth for streaming operations | Throughput (MB/sec) | 
HPL | Floating-point compute performance (FLOPS) | GFLOPS | 
cublas Matrix Multiplication | GPU compute performance for linear algebra operations | GFLOPS | 
LLM Perf | LLM inference throughput/latency | Throughput (tokens/sec) | GPT OSS 120B

## Slide 10: Success Criteria
Outcome | Requirements
PASS | The results for each benchmark are within the desired threshold of NVIDIA’s virtualization control stack performance baseline
FAIL | One/more test results deviate beyond the prescribed threshold from NVIDIA’s virtualization control stack performance baseline

## Slide 11: x86 Certification Track- Reference Software Stacks

## Slide 12: Single node x86 Certification SW Stack
Category | Bare Metal Baseline | Virtualized Control Stack- Single Node 8 GPU Passthrough VM
Server | DGX H100 | DGX H100
Switch Connectivity | TOR (100 Gb) | TOR (100 Gb)
GPUs | 8x H100 | 8x H100
NICs | 4x CX-7 | 4x CX-7
DPU | 1x BF3 | 1x BF3
Platform OS | Ubuntu 24.04 LTS | N/A
Platform OS Kernel |  | 5.15.0-153-generic
Hyperthreading | ON | ON
Hypervisor | N/A | Ubuntu 22.04 LTS
KVM/QEMU | N/A | 6.2.0
Fabric Manager Version | N/A | N/A
Guest OS | N/A | Ubuntu 24.04 LTS
Datacenter Driver Version | R580 | R580
Container Runtime | containerd | containerd
K8s | K8s 1.31 | K8s 1.31
GPU Operator | 25.3.0 | 25.3.0
Network Operator | N/A | N/A
LLM NIM | Llama-3.3-70B | Llama-3.3-70B

## Slide 13: Multi Node x86 Certification SW Stack
Category | Multi-node Bare metal Baseline | Virtualized Control Stack– Multi Node 8-GPU Passthrough VM
Server | DGX H100 | DGX H100
Switch Connectivity | TOR (100 Gb) | TOR (100 Gb)
GPUs | 8x H100 | 8x H100
NICs | 4x CX-7 | 4x CX-7
DPU | 1x BF3 | 1x BF3
Platform OS | Ubuntu 24.04.3 LTS | Ubuntu 24.04.3 LTS
Platform OS Kernel | 6.11.0-1027-oem | 6.8.0-101-generic
Hyperthreading | ON | ON
Hypervisor | N/A | Ubuntu 22.04 LTS
KVM/QEMU | QEMU emulator version 8.2.2 | QEMU emulator version 8.2.2
Fabric Manager Version | 580.126.09 | 580.126.09
Guest OS | N/A | Ubuntu 24.04 LTS
Datacenter Driver Version | 580.126.09 | 580.126.09
Container Runtime | containerd | containerd
K8s | K8s 1.33 | K8s 1.33
GPU Operator | 25.3.2 | 26.3.0
Network Operator | N/A | N/A
LLM NIM | DeepSeek-R1 671B | DeepSeek-R1 671B

## Slide 14: Closing

## Slide 15: Next Steps
NVIDIA is targeting Q3 (July) to launch this program and would love to have Red Hat successfully complete certification before launch.
NVIDIA LaunchPad will provide compute access needed for running validation on systems aligned with NVIDIA’s roadmap:
  Next steps involve targeting a branch of OCP + OpenShift Virtualization (OSV) and facilitating hardware access to Red Hat to begin validation

## Slide 16: x86 Performance Certification Summary
Phase | VM Config | Performance Benchmarks | Evaluation Outcome
Phase I- Single Node | Single 8-GPU VM configured in full passthrough | Core Tests LLM Perf | PASS = Partner can move forward with Phase II FAIL = NVIDIA team to evaluate results on a case by case basis. Partner to troubleshoot their stack based on NVIDIA’s recommendations and re-run the tests
Phase II- Multi Node | Two identical 8-GPU VMs configured in full passthrough and deployed on two separate DGX/HGX nodes | Core Tests LLM Perf GPU Direct RDMA | PASS = Partner is certified to run 8 GPU VMs with near-bare metal performance for AI inferencing workloads on NVIDIA x86 systems FAIL = NVIDIA team to evaluate results on a case by case basis.

## Slide 17: Thank You